## Slide 2
UDP (User Datagram Protocol)
è un protocollo a livello applicazione che prevede un sottostrato che usa IP.
Permette la trasmissione a pacchetti ma non ne garantisce la consegna e l’unicità.
Per applcazioni in cui tale caratteristica è importante va usato il TCP (Transmission Control Protocol)
Endpoint (detto Host in ambiente Internet) è una entità detta NODO identificato da informazioni a livello di trasporto che possono includere una porta UDP.

## Slide 3: URL ( è possibile considerare anche URI come stessa cosa)
https://tools.ietf.org/html/rfc1738#section-3.10
Esistono diversi schemi di accesso ad una risorsa e URL è uno di questi.URL usato per localizzare una risorsa.
Per ogni URL va definito il metodo di «accesso» alla risorsa.
Schema di base:
<scheme>:<scheme-specific-part>
Alcuni schemi sono URL come ad es ftp e http : questi possono avere nomi gerarchici ( xxx/yyy/eee)
Schemi URL per l’uso diretto di protocolli IP-based su di un particolare host su Internet usano uno schema ben preciso:
//<user>:<password>@<host>:<port>/<url-path>
Alcune parti possono essere omesse
Il «//» indica un percorso compliant con schema Internet.
Il modo di utilizzo di tale schema dipende dal protocollo.
Es: <URL:ftp://@host.com/>
ftp > File Transfer protocol
http > Hypertext Transfer Protocol
gopher > The Gopher protocol
mailto > Electronic mail address
news > USENET news
nntp > USENET news using NNTP access
telnet > Reference to interactive sessions
wais > Wide Area Information Servers
file > Host-specific file names
prospero > Prospero Directory Service
https://www.iana.org/assignments/uri-schemes/uri-schemes.xhtml

## Slide 4: Protocolli per IoT - CoAP
Constrained Application Protocol (CoAP) : was designed to translate the HTTP model so that it could be used in restrictive device and network environments
E’ specializzato per l’uso di dispositive con poca Potenza (es micro a 8bit con poca ROM RAM) e reti a bassa qualità/prestazione (come ad es IPv6 over LowPower Wireless Personal Area Networwk 6LowPAN)
Focalizzato a M2M (machine to machine) con funzioni built-in discovery, multicast support, and asynchronous message exchanges
Si interfaccia facilmente con Http.
https://tools.ietf.org/html/rfc7252
A CoAP request is equivalent to that of HTTP and is sent by a client to request an action (using a Method Code) on a resource (identified by a URI) on a server.
Usa UDP e permette anche il broadcast.

## Slide 5: Protocolli per IoT - MQTT

## Slide 6: Protocolli per IoT -

## Slide 7: Protocolli per IoT -